BAMBURGH RESEARCH PROJECT

SEA VIEW,

BILTON,

NORTHUMBERLAND

REPORT OF ARCHAEOLOGICAL

MONITORING AND RECORDING

Compiled for Mr Julian Bard by The Bamburgh Research Project: Commercial Projects Section

# BRP 07/17									January 2008

Contents:

SUMMARY										3

- Introduction								4

2.0	THE SITE									4

2.1	Location									4

##### 2.2	Archaeological background							4

3.0	METHODOLOGY								5

3.1	Monitoring during excavation						5

3.2	Contingency									5

3.3	General standards								5

4.0	RESULTS									6

4.1	Monitoring during excavation						6

5.0	CONCLUSIONS								7

REFERENCES									8

APPENDIX I	WSI									9

Figure 1	Site location plan

Figure 2	Plan of the new structural extension

Plate 1: 	Eastern construction trench, facing north

# SUMMARY

This report has been compiled by The Bamburgh Research Project for Mr Julian Board and sets out the results of archaeological monitoring undertaken during December 2007.

The development comprised the construction of two extensions to Sea View, Bilton. The first, a small porch extension measuring 4.7m east to west by 1.7m north to south on the north side of the building was not subject to a watching brief as previous ground disturbance has indicated that no archaeology was present in this area. The second extension, 5.6m east to west by 8.7m north to south, was attached to the east side of the building and was subject to archaeological monitoring. The site is located on the north side of the road that passes through the village of Bilton, Northumberland. The village lies 2km west of Alnmouth and 1km to the west of the A1068 (NGR NU 2279 1085) (Figure 1).

Topsoil comprised a very dark grey-brown sandy silt up to 0.4m thick over a yellow-brown sand with some silt. The excavation of the southern line of foundations revealed a waste service pipe at the base of the trench extending along its full length. Excavation of the east and north sides of the foundation revealed a single modern feature, a further waste service pipe. The pipe extended across the eastern foundation trench on an east to west alignment. The backfill of this trench contained a number of roughly squared stones clearly from a building. No further indication of occupational material was present in the two trenches and no finds recovered.

Although the site lay within the area of Bilton Village, known to have been in existence since the medieval period, no indication of occupation was present on the site, though the presence of building stone in the service trench backfill would indicate structural activity in the general vicinity.

SEA VIEW,

BILTON,

NORTHUMBERLAND

REPORT OF ARCHAEOLOGICAL MONITORING

- Introduction

    - This report has been compiled by The Bamburgh Research Project, Commercial Section for Mr Julian Board. The document sets out the results of the monitoring of the groundworks associated with the construction of an extension to Sea View, Bilton, Northumberland.

    - The work was undertaken in compliance with a Written Schedule of Investigation compiled by the Bamburgh Research Project in December 2007 in response to a brief issued by the Northumberland County Council Conservation Team. The NCCCT reference number is: A25/2; 7214 and the planning reference is A/2007/0335.

2.0 	THE SITE

2.1	Location

2.1.1	The site is located on the north side of the road that passes through the village of Bilton, Northumberland. The village lies 2km west of Alnmouth and 1km to the west of the A1068 (NGR NU 2279 1085) (Figures 1 and 2).

  - Archaeological Background

    - The settlement at Bilton, in the parish of Lesbury, was a part of the medieval Barony of Alnwick created in the early 12th century during the reign of Henry I. The township of Bilton was in existence from 1296 when it is first mentioned in documentary records. A township plan of 1586 depicts the manor at the north-west end of the village which comprised two rows of tofts set along the road through the village. A further plan of 1722 shows a substantial village set within an enclosed landscape. The rationalisation of the estate resulted in the shrinkage of the village by 1807, when it is depicted showing only the northern row of tofts.

    - The first edition Ordnance Survey map depicts a village laid out along the northern side of the road with a further village road parallel to the north cutting through the northern part of the tofts.

3.0	METHODOLOGY

# 3.1	Monitoring during excavation

3.1.1	A suitably experienced archaeologist, familiar with the archaeological background to the site, was to be present to record any items of interest that were revealed. The excavation was undertaken by hand. All work was carried out in compliance with the codes of practice of the Institute of Field Archaeologists (IFA) and followed the IFA Standards for Watching Briefs. The work undertaken conformed to the methodology listed below.

3.2	Contingency

3.2.1	In the event of the discovery of unexpected archaeological remains, work was to cease and the County Archaeological Officer/representative of the developer would be notified in order that an assessment of the importance of the remains and any provision for their recording could be made.

    - A contingency for excavation comprising up to 20 person days could have been invoked following consultation with the County Archaeologist.

3.3	General standards

3.3.1	All archaeological features identified during the monitoring, or following the implementation of the contingency would be sample excavated according to their type and form:

50% of all discrete features.

50% of waterlogged deposits.

25% of stratified deposits.

25% of the area of linear/curvilinear features with a non-uniform fill

10% of the area of linear/curvilinear features with a uniform fill

3.3.2	A 40 litre bulk palaeoenvironmental sample would be taken from all features recognised as suitable for the preservation of palaeoenvironmental remains.

3.3.3	Secure contexts would be sampled for dating where appropriate, whether on site or as sub samples of bulk samples.

3.3.4	Pottery and Animal Bone would be collected as bulk samples whilst significant artefacts would be three-dimensionally recorded prior to processing. All finds would be recorded and processed according to the BRP system and submitted for post-excavation assessment. Finds recovery and storage strategies were in accordance with published guidelines (English Heritage 1995 and IFA Guidelines for Finds Work). Had artefacts of gold or silver been recovered the would be treated in accordance with the 1996 Treasure Act and appropriate procedures would be followed.

3.3.5	In the event of Human burials being revealed they would be left in situ and treated in an appropriate manner. Consultation with the County Archaeological Officer would be sought to determine further action.

3.3.6	Any archaeological features encountered would be hand-cleaned, excavated and recorded:

- A photographic record of the site was taken using black and white print, colour slide film at 35mm format. In addition a digital photographic record was compiled.

- A written description of features was compiled using the BRP pro forma context recording system.

3.3.8	Arrangements will be made with the appropriate museum for the deposition of the site archive within 6 month of the completion of the post-excavation report.

4.0	RESULTS

  - Monitoring during excavation

4.1.1	Topsoil comprised a very dark grey-brown sandy silt up to 0.4m thick over a yellow-brown subsoil made-up of sand with some silt. The excavation of the southern line of foundations revealed a waste service pipe at the base of the trench extending along its full length. Excavation of the east and north sides of the foundation revealed a single modern feature, a further waste service pipe. The pipe extended across the eastern foundation trench on an east to west alignment. The backfill of this trench contained a number of roughly squared stones clearly from a building (Figure 2). No further indication of occupational material was present in the two trenches and no finds recovered.

- CONCLUSIONS

  - Although the site lay within the area of Bilton Village, known to have been in existence since the medieval period, no indication of occupation was present on the site, though the presence of building stone in the service trench backfill would indicate structural activity in the general vicinity.

5.2	The topography of the village is somewhat unusual in that the village buildings lie on the relatively steep slope above the road. It is possible that the position of the buildings has moved over time, which would account for the absence of archaeological material within the development area.

Text and illustrations: Graeme Young

BRP 07/17									December 2007

REFERENCES

Published and unpublished sources

BRP			Finds Manual, 2000

BRP			Health and Safety Document

English Heritage	Management of Archaeological Projects 2, 1991.

English Heritage	A strategy for the Care and Investigation of Finds. Ancient Monuments Laboratory, 1995.

IFA 2000 		Code of Conduct

IFA 2001 		Standard and Guidance for Archaeological Field Evaluation.

APPENDIX I

SEA VIEW,

BILTON,

NORTHUMBERLAND

ARCHAEOLOGICAL WATCHING BRIEF

WRITTEN SCHEDULE OF INVESTIGATION

- Introduction

1.0.1	This Written Schedule of Investigation has been compiled by The Bamburgh Research Project for Mr Julian Board, regarding the development at Sea View, Bilton, Northumberland, during December 2007. The document sets out the project design for an archaeological watching brief of groundworks associated with the extension of an existing building.

    - The Written Schedule of Investigation details the proposed scheme of works for the watching brief and has been prepared in order to fulfil a requirement for the planning application, as laid out in the brief issued by The Northumberland County Council Conservation Team. The NCCCT reference number: A25/2; 7214 and the planning reference is A/2007/0335.

2.0 	THE SITE

2.1	Location

2.1.1	The site is located on the north side of the road that passes through the village of Bilton, Northumberland. The village lies 2km west of Alnmouth and 1km to the west of the A1068 (NGR NU 2279 1085) (Figure 1).

2.2	Archaeological Background to the site

    - The settlement at Bilton, in the parish of Lesbury, was a part of the medieval Barony of Alnwick created in the early 12th century. Bilton was in existence from 1296 when it is first mentioned in documentary records. A township plan of 1586 depicts the manor at the north-west end of the village which comprised two rows of tofts set along the road through the village. A further plan of 1722 shows a substantial village set within an enclosed landscape. The rationalisation of the estate resulted in the shrinkage of the village by 1807, when it is depicted showing only the northern row of tofts.

    - The first edition Ordnance Survey map depicts a village laid out along the northern side of the road with a further village road parallel to the north cutting through the northern part of the tofts.

  - Impact of the development

    - The development involves the construction of additions to the present building comprising the construction of new extensions to the east and north. The eastern extension represents the major part of the development and measures 5.6m east to west by 8.7m north to south. The northern extension is much smaller and measures 4.7m east to west by 1.7m north to south. The foundations of the new structure (marked in red) are to be excavated to a depth of 900mm below ground level (Figure 2).

    - Although there is no direct evidence of archaeological remains within the site area the location of the development within a known medieval settlement and immediately to the north of the road indicates that there is potential for the groundworks associated with the development to disturb archaeological remains associated with the medieval tofts.

3.0	OBJECTIVES

    - In the light of the potential for the construction work to impact upon preserved archaeological remains it is proposed that a continuous watching brief be conducted during the ground work in accordance with the specification laid out in the brief issued by the County Council Conservation Team.

4.0	METHODOLOGY

4.1	Watching brief during excavation

    - During the excavation of the foundations, service trenches, a suitably experienced archaeologist, familiar with the archaeological background to the site, will be present to record any items of interest that area revealed by these excavations. Where appropriate all excavation and stripping will be carried out by a machine using a toothless ditching bucket. All work will be carried out in compliance with the codes of practice of the Institute of Field Archaeologists (IFA) and should follow the IFA Standards for Watching Briefs. This watching brief will conform to the following methodology.

4.2	Contingency

    - In the event of the discovery of unexpected archaeological remains over and above those predicted by previous archaeological work on the adjoining site, work will cease and the County Archaeological Officer/representative of the developer will be notified in order that an assessment of the importance of the remains and any provision for their recording may be made.

    - A contingency for excavation comprising up to 20 person days can be invoked following consultation with the County Archaeologist.

4.3	General standards

4.3.1	All archaeological features identified during the monitoring, or following the implementation of the contingency will be sample excavated according to their type and form:

50% of all discrete features.

50% of waterlogged deposits.

25% of stratified deposits.

25% of the area of linear/curvilinear features with a non-uniform fill

10% of the area of linear/curvilinear features with a uniform fill

4.3.2	A 40 litre bulk palaeoenvironmental sample will be taken from all features recognised as suitable for the preservation of palaeoenvironmental remains.

4.3.3	Secure contexts will be sampled for dating where appropriate, whether on site or as sub samples of bulk samples. Any concentrations of charcoal or other carbonised material recovered on site will usually be retained.

4.3.4	Pottery and Animal Bone will be collected as bulk samples whilst significant artefacts will be three-dimensionally recorded prior to processing. All finds will be recorded and processed according to the BRP system and submitted for post-excavation assessment. Finds recovery and storage strategies will be in accordance with published guidelines (English Heritage 1995 and IFA Guidelines for Finds Work). Should artefacts of gold or silver covered by the 1996 Treasure Act be recovered, appropriate procedures will be followed.

4.3.5	In the event of Human burials being revealed they will be left in situ and treated in an appropriate manner. After consultation with the County Archaeological Officer, if excavation is required, work will comply with the relevant home Office regulations.

4.3.6	Any archaeological features encountered will be hand-cleaned, excavated and recorded:

- A photographic record of the site will be taken using black and white print, colour slide film at 35mm format. In addition a digital photographic record will be compiled.

- A written description of features will be recorded using the BRP pro forma context recording system.

- All features will be drawn at an appropriate scale using pre-printed permatrace. Plans will normally be drawn at a scale of 1:20 and sections at a scale of 1:10.

4.3.7	All archaeological features and horizons will be accurately tied into the Ordnance Survey grid. All levels will be tied in to Ordnance Datum.

4.3.8	Arrangements will be made with the appropriate museum for the deposition of the site archive within 6 month of the completion of the post-excavation report.

5.0	MONITORING

5.0.1	Access will be made available at all reasonable times to the archaeological representatives of the Northumberland County council Conservation Team to inspect the excavation site.

5.0.2	Access to the site will be on the basis of prior notification and subject to any relevant health and safety considerations.

6.0	POST-EXCAVATION WORK, ARCHIVE AND REPORT COMPILATION

6.0.1	On completion of the excavation an assessment of the site records and finds will be undertaken in accordance with English Heritage (1991) guidelines. This will include:

- collation of all site records

- compilation of a report

- production of context, photographic, finds and illustration databases

- analysis of the finds assemblage by relevant specialists

- environmental assessment of selected bulk samples

6.0.2	The assessment report, with each page and paragraph numbered and with cross referenced illustrations, will include:

- summary of the project background

- site location

- methodology

- results of the watching brief

- site location plans and illustrations of results at appropriate scales

- interpretation of the results in an appropriate context

- post-excavation assessment of the site archive

- catalogue and assessment of the artefactual archive

- catalogue and assessment of the faunal remains

- catalogue and assessment of the palaeoenvironmental samples recovered

- appendix containing a list and summary of each recorded context

6.0.3	A copy of the report should be submitted by the archaeologist to the commissioning client, and the County SMR within 2 months of completion of the work. A summary will be prepared for 'Archaeology in Northumberland' and an article will be submitted to a local or national journal if appropriate.

6.0.4	The site archive will be prepared to the standard specified in the Management of Archaeological Projects, appendix 3 (HBMC 1991) and in accordance with the Guidelines for the Preparation of Excavation Archives for Long Term Storage (UKIC 1990).  A summary account of the context record will be included and written by the supervising archaeologist. The archive will be deposited at the specified museum within 6 months of completion of the work on site.

6.0.4	An online OASIS form will be completed for the project as part of the post-excavation assessment process.

7.0	PERSONNEL

7.0.1	The designated project manager Graeme Young, is one of the five directors of the Bamburgh Research Project. A graduate of Newcastle University, with 18 years of experience in field archaeology including directing a number of excavations of urban medieval sites in Newcastle and Durham. He is an Associate Member of the Institute of Field Archaeologists.

7.0.2	Additional field staff, with appropriate archaeological experience, will be engaged as required.

8.0	SUB-CONTRACTED SPECIALISTS

    - Although it is not possible to predict the range of artefacts that may be recovered provision has been made for the analysis of the most common artefacts.

Material			Specialist

Medieval pottery			Jenny Vaughan

Post-medieval pottery		Jenny Vaughan

Prehistoric pottery		Blaise Vyner

Roman Pottery			Blaise Vyner/ John Dore

Animal bone			Durham University Archaeological Services

Palaeoenvironmental		Durham University Archaeological Services

Conservation			Karen Barker

9.0	HEALTH AND SAFETY

9.0.1	The Bamburgh Research Project complies with the 1974 Health and Safety Act and its subsequent amendments in all its operations. The SCAUM manual and the Bamburgh Research Project Health and Safety Policy Document is followed for all site works. A designated and appropriately trained first aider is present at all times during working hours. A First Aid kit, Accident Book and telephone are provided for each project. Safety footwear is mandatory on all excavation sites. Where required safety helmets and reflective jackets are provided. It is policy for a vehicle to be present at an excavation and staff must be appropriately equipped for bad weather.

9.0.2	All staff undergo a safety induction prior to commencing work on site. A written risk assessment is undertaken specific for each site. The safety assessment is reviewed on a daily basis and changes to the working conditions monitored continually during adverse weather conditions.

Text: Graeme Young.

BRP 07/17									December 2007

REFERENCES

Published and unpublished sources

BRP			Finds Manual, 2000

BRP			Health and Safety Document

English Heritage		Management of Archaeological Projects 2, 1991.

English Heritage	A strategy for the Care and Investigation of Finds. Ancient Monuments Laboratory, 1995.

IFA 2000 		Code of Conduct

IFA 2001 		Standard and Guidance for Archaeological Watching Briefs.

# Plate1:  Eastern construction trench, facing north