BAMBURGH RESEARCH PROJECT

LAND AT EAST MOLESDEN FARM,

MITFORD,

NORTHUMBERLAND

REPORT OF ARCHAEOLOGICAL

MONITORING AND RECORDING

Compiled for Mr A.J. Taylor by The Bamburgh Research Project: Commercial Projects Section

# BRP 08/10									October 2008

Contents:

SUMMARY										3

- Introduction								4

2.0	THE SITE									4

2.1	Location									4

##### 2.2	Archaeological background							4

3.0	METHODOLOGY								5

3.1	Monitoring during excavation						5

3.2	General standards								5

4.0	RESULTS									6

4.1	Monitoring during excavation						6

5.0	CONCLUSIONS								7

REFERENCES									8

APPENDIX I	WSI									9

Figure 1	Location of the development

Figure 2	Location of the new construction

# Plate 1		The excavated foundation trenches, facing west

# Plate 2		Excavated trench section, facing west

# SUMMARY

This report has been compiled by The Bamburgh Research Project for Mr A. J. Taylor and sets out the results of the archaeological monitoring undertaken in October 2008, during the groundworks associated with the construction of a new dwelling on land at East Molesden Farm, Mitford, Northumberland (NGR NZ 14938419) (Figures 1 and 2).

The topsoil on the site had been stripped prior to the commencement of the watching brief. Excavation of the foundation trenches was undertaken under archaeological monitoring on the 13th October 2008. The main building trenches were excavated to a width of 0.75m and the internal partition trenches to 0.45m, both were excavated to a depth of 0.5m below ground level. No features of archaeological interest were identified and no finds were present.

The site of the new dwelling lay in an open area of ground to the east of the present farm building. Stripping of the topsoil had occurred prior to the commencement of the watching brief. This limited the amount of evidence available to interpret the site, however the absence of any finds from the monitoring of a considerable excavated volume would suggest that the site was located in an area of the settlement with little or no archaeological activity.

LAND AT EAST MOLESDEN FARM,

MITFORT,

NORTHUMBERLAND

REPORT OF ARCHAEOLOGICAL MONITORING

- Introduction

    - This report has been compiled by The Bamburgh Research Project, Commercial Section for Mr A. J. Taylor. The document sets out the results of the monitoring of the groundworks associated with the construction of a new dwelling on land adjacent to East Molesden Farm, Mitford, Northumberland, undertaken during the 13th of October 2008.

1.0.2	The work was undertaken in compliance with a Written Schedule of Investigation compiled by the Bamburgh Research Project in September 2008 in response to a brief issued by the Northumberland County Council Conservation Team. The NCCCT reference number is: CM14/1; 4375 and the Planning application number is: 05/D/037. The OASIS record number is: bamburgh1-50314.

2.0 	THE SITE

2.1	Location

2.1.1	East Molesden Farm is located on the north side of the road within the hamlet of East Molesden, which lies on an unclassified road between Mitford and Meldon, some 1km south of the River Wansbeck and 5km south west of Morpeth, Northumberland (NGR NZ 14938419) (Figures 1 and 2).

  - Archaeological background

    - The village of East Molesden is first mentioned in the documentary record in AD 1296. The call roll for Mitford, in 1666, listed five tenants and the hearth tax mentioned eight houses. By the time of the compilation of Armstrong’s Map of 1769 only three farmsteads survived. The first edition Ordnance Survey c. 1860 depicts the site as an open plot of land.

## 2.2.2	Aerial photographic analysis indicates that the houses that survive on the north side of the road form the northern row of tenements with the southern row south of the road and east of the small burn that passes through the settlement and around which it is likely to have been focussed. Ridge and furrow cultivation was traced extending up to the northern row of tenements, likely forming part of the infield for the medieval hamlet.

3.0	METHODOLOGY

# 3.1	Monitoring during excavation

3.1.1	A suitably experienced archaeologist, familiar with the archaeological background to the site, was present to record any items of interest that were revealed. All work was carried out in compliance with the codes of practice of the Institute of Field Archaeologists (IFA) and followed the IFA Standards for Watching Briefs. The work undertaken conformed to the methodology listed below.

3.2	General standards

3.2.1	All archaeological features identified during the monitoring, would be sample excavated according to their type and form:

50% of all discrete features.

50% of waterlogged deposits.

25% of stratified deposits.

25% of the area of linear/curvilinear features with a non-uniform fill

10% of the area of linear/curvilinear features with a uniform fill

3.2.2	A 40 litre bulk palaeoenvironmental sample would be taken from all features recognised as suitable for the preservation of palaeoenvironmental remains.

3.2.3	Secure contexts would be sampled for dating where appropriate, whether on site or as sub samples of bulk samples.

3.2.4	Pottery and Animal Bone would be collected as bulk samples whilst significant artefacts would be three-dimensionally recorded prior to processing. All finds would be recorded and processed according to the BRP system and submitted for post-excavation assessment. Finds recovery and storage strategies were in accordance with published guidelines (English Heritage 1995 and IFA Guidelines for Finds Work). Had artefacts of gold or silver been recovered they would be treated in accordance with the 1996 Treasure Act and appropriate procedures would be followed.

3.2.5	In the event of Human burials being revealed they would be left in situ and treated in an appropriate manner. Consultation with the County Archaeological Officer would be sought to determine further action.

3.2.6	Any archaeological features encountered would be hand-cleaned, excavated and recorded:

- A photographic record of the site was taken using black and white print, colour slide film at 35mm format. In addition a digital photographic record was compiled.

- A written description of features was compiled using the BRP pro forma context recording system.

3.2.8	Arrangements will be made with the appropriate museum for the deposition of the site archive within 6 month of the completion of the post-excavation report.

4.0	RESULTS

  - Monitoring during excavation

4.1.1	The topsoil on the site had been stripped prior to the commencement of the watching brief to reveal a light red-brown silty clay subsoil. Excavation of the foundation trenches was undertaken under archaeological monitoring by a 360-degree excavator with a toothless bucket on the 13th October 2008. The main building trenches were excavated to a width of 0.75m and the internal partition trenches to 0.45m, both were excavated to a depth of 0.5m below ground level. No features of archaeological interest were identified and no finds were present.

.

5.0	CONCLUSIONS

    - The site of the new dwelling lay in an open area of ground to the east of the present farm building. Stripping of the topsoil had occurred prior to the commencement of the watching brief. This limited the amount of evidence available to interpret the site, however the absence of any finds from the monitoring of a considerable excavated volume would suggest that the site was located in an area of the settlement with little or no archaeological activity.

Text and illustrations: Graeme Young

BRP 08/10									October 2008

REFERENCES

Published and unpublished sources

BRP			Finds Manual, 2000

BRP			Health and Safety Document

English Heritage	Management of Archaeological Projects 2, 1991.

English Heritage	A strategy for the Care and Investigation of Finds. Ancient Monuments Laboratory, 1995.

IFA 2000 		Code of Conduct

APPENDIX I

LAND AT EAST MOLESDEN FARM,

MITFORD,

NORTHUMBERLAND

ARCHAEOLOGICAL WATCHING BRIEF

WRITTEN SCHEDULE OF INVESTIGATION

- Introduction

1.0.1	This Written Schedule of Investigation has been compiled by The Bamburgh Research Project for Mr Alec J. Taylor, regarding the construction of a detached dwelling on land at East Molesden Farm, Mitford, Northumberland, during September 2008. The document sets out the project design for an archaeological watching brief to be conducted during groundworks associated with the construction.

    - The Written Schedule of Investigation details the proposed scheme of works for the watching brief and has been prepared in order to fulfil a requirement for the planning application, as laid out in the brief issued by The Northumberland County Council Conservation Team. The NCCCT reference number is: CM14/1; 4375 and the Planning application number is: 05/D/037.

2.0 	THE SITE

2.1	Location

2.1.1	East Molesden Farm is located on the north side of the road within the hamlet of East Molesden, which lies on an unclassified road between Mitford and Meldon, some 1km south of the River Wansbeck and 5km south west of Morpeth, Northumberland (NGR NZ 14938419) (Figures 1 and 2).

2.2	Archaeological background to the site

    - The village of East Molesden is first mentioned in the documentary record in AD 1296. The call roll for Mitford, in 1666, listed five tenants and the hearth tax mentioned eight houses. By the time of the compilation of Armstrong’s Map of 1769 only three farmsteads survived. The first edition Ordnance Survey c. 1860 depicts the site as an open plot of land.

## 2.2.2	Aerial photographic analysis indicates that the houses that survive on the north side of the road form the northern row of tenements with the southern row south of the road and east of the small burn that passes through the settlement and around which it is likely to have been focussed. Ridge and furrow cultivation was traced extending up to the northern row of tenements, likely forming part of the infield for the medieval hamlet.

    - Impact of the development

    - The development involves the construction of a detached dwelling on an area of open ground that forms part of East Molesden Farm. The new building measures 15m east to west by 8.44m north to south. The main foundation for the building will be 0.5m wide and is intended to be of an average depth of 0.75m and should not exceed 1.0m. Internal partition foundations will measure 0.45m wide and will be excavated to a similar depth. The building will be connected to the existing services. No details of the line or depth of the proposed service trenches is available at present. A hard standing area for parking will be constructed to the south west of the new building, connecting to the present access road (Figure 2).

    - The site is located within the area likely to have been occupied by the northern row of tenements of the medieval hamlet. Although it is not certain how densely occupied these tenements were the excavation of the foundations of the new building, predicted to extend to a depth of c. 750mm,the service trenches and the new hard standing area clearly have the potential to impact on preserved archaeological stratigraphy.

3.0	OBJECTIVES

    - In the light of the potential for the construction work to impact, in places, upon preserved archaeological remains it is proposed that a continuous watching brief be conducted during the ground work in accordance with the specification laid out in the brief issued by the County Council Conservation Team.

4.0	METHODOLOGY

4.1	Watching brief during excavation

    - During all excavation activity for the new development a suitably experienced archaeologist, familiar with the archaeological background to the site, will be present to record any items of interest that are revealed. Where appropriate all excavation and stripping will be carried out by a machine using a toothless ditching bucket. All work will be carried out in compliance with the codes of practice of the Institute of Field Archaeologists (IFA) and should follow the IFA Standards for Watching Briefs. This watching brief will conform to the following methodology.

4.2	Contingency

    - In the event of the discovery of unexpected archaeological remains over and above those predicted by previous archaeological work on the adjoining site, work will cease and the County Archaeological Officer/representative of the developer will be notified in order that an assessment of the importance of the remains and any provision for their recording may be made.

    - A contingency for excavation comprising up to 5 person days can be invoked following consultation with the County Archaeologist.

4.3	General standards

4.3.1	All archaeological features identified during the monitoring, or following the implementation of the contingency will be sample excavated according to their type and form:

50% of all discrete features.

50% of waterlogged deposits.

25% of stratified deposits.

25% of the area of linear/curvilinear features with a non-uniform fill

10% of the area of linear/curvilinear features with a uniform fill

4.3.2	A 40 litre bulk palaeoenvironmental sample will be taken from all features recognised as suitable for the preservation of palaeoenvironmental remains.

4.3.3	Secure contexts will be sampled for dating where appropriate, whether on site or as sub samples of bulk samples. Any concentrations of charcoal or other carbonised material recovered on site will usually be retained.

4.3.4	Pottery and Animal Bone will be collected as bulk samples whilst significant artefacts will be three-dimensionally recorded prior to processing. All finds will be recorded and processed according to the BRP system and submitted for post-excavation assessment. Finds recovery and storage strategies will be in accordance with published guidelines (English Heritage 1995 and IFA Guidelines for Finds Work). Should artefacts of gold or silver covered by the 1996 Treasure Act be recovered, appropriate procedures will be followed.

4.3.5	In the event of Human burials being revealed they will be left in situ and treated in an appropriate manner if possible. Any burial requiring excavation will be exposed, recorded and lifted in total. After consultation with the County Archaeological Officer, if excavation is required, work will comply with the relevant home Office regulations.

4.3.6	Any archaeological features encountered will be hand-cleaned, excavated and recorded:

- A photographic record of the site will be taken using black and white print, colour slide film at 35mm format. In addition a digital photographic record will be compiled.

- A written description of features will be recorded using the BRP pro forma context recording system.

- All features will be drawn at an appropriate scale using pre-printed permatrace. Plans will normally be drawn at a scale of 1:20 and sections at a scale of 1:10.

4.3.7	All archaeological features and horizons will be accurately tied into the Ordnance Survey grid. All levels will be tied in to Ordnance Datum.

4.3.8	Arrangements will be made with the appropriate museum for the deposition of the site archive within 6 month of the completion of the post-excavation report.

5.0	MONITORING

5.0.1	Access will be made available at all reasonable times to the archaeological representatives of the Northumberland County council Conservation Team to inspect the excavation site.

5.0.2	Access to the site will be on the basis of prior notification and subject to any relevant health and safety considerations.

6.0	POST-EXCAVATION WORK, ARCHIVE AND REPORT COMPILATION

6.0.1	On completion of the excavation an assessment of the site records and finds will be undertaken in accordance with English Heritage (1991) guidelines. This will include:

- collation of all site records

- compilation of a report

- production of context, photographic, finds and illustration databases

- analysis of the finds assemblage by relevant specialists

- environmental assessment of selected bulk samples

6.0.2	The assessment report, with each page and paragraph numbered and with cross referenced illustrations, will include:

- summary of the project background

- site location

- methodology

- results of the watching brief

- site location plans and illustrations of results at appropriate scales

- interpretation of the results in an appropriate context

- post-excavation assessment of the site archive

- catalogue and assessment of the artefactual archive

- catalogue and assessment of the faunal remains

- catalogue and assessment of the palaeoenvironmental samples recovered

- appendix containing a list and summary of each recorded context

6.0.3	A copy of the report should be submitted by the archaeologist to the commissioning client, and the County SMR within 2 months of completion of the work. A summary will be prepared for 'Archaeology in Northumberland' and an article will be submitted to a local or national journal if appropriate.

6.0.4	The site archive will be prepared to the standard specified in the Management of Archaeological Projects, appendix 3 (HBMC 1991) and in accordance with the Guidelines for the Preparation of Excavation Archives for Long Term Storage (UKIC 1990).  A summary account of the context record will be included and written by the supervising archaeologist. The archive will be deposited at the specified museum within 6 months of completion of the work on site.

6.0.4	An online OASIS form will be completed for the project as part of the post-excavation assessment process.

7.0	PERSONNEL

7.0.1	The designated project manager Graeme Young, is one of the five directors of the Bamburgh Research Project. A graduate of Newcastle University, with 18 years of experience in field archaeology including directing a number of excavations of urban medieval sites in Newcastle and Durham. He is an Associate Member of the Institute of Field Archaeologists.

7.0.2	Additional field staff, with appropriate archaeological experience, will be engaged as required.

8.0	SUB-CONTRACTED SPECIALISTS

    - Although it is not possible to predict the range of artefacts that may be recovered provision has been made for the analysis of the most common artefacts.

Material			Specialist

Medieval pottery		Jenny Vaughan

Post-medieval pottery		Jenny Vaughan

Prehistoric pottery		Blaise Vyner

Roman Pottery			Blaise Vyner

Animal bone			Durham University Archaeological Services

Palaeoenvironmental		Durham University Archaeological Services

Conservation			Karen Barker

9.0	HEALTH AND SAFETY

9.0.1	The Bamburgh Research Project complies with the 1974 Health and Safety Act and its subsequent amendments in all its operations. The SCAUM manual and the Bamburgh Research Project Health and Safety Policy Document is followed for all site works. A designated and appropriately trained first aider is present at all times during working hours. A First Aid kit, Accident Book and telephone are provided for each project. Safety footwear is mandatory on all excavation sites. Where required safety helmets and reflective jackets are provided. It is policy for a vehicle to be present at an excavation and staff must be appropriately equipped for bad weather.

9.0.2	All staff undergo a safety induction prior to commencing work on site. A written risk assessment is undertaken specific for each site. The safety assessment is reviewed on a daily basis and changes to the working conditions monitored continually during adverse weather conditions.

Text: Graeme Young.

BRP 08/10									September 2008

REFERENCES

Published and unpublished sources

BRP			Finds Manual, 2000

BRP			Health and Safety Document

English Heritage		Management of Archaeological Projects 2, 1991.

English Heritage	A strategy for the Care and Investigation of Finds. Ancient Monuments Laboratory, 1995.

IFA 2000 		Code of Conduct

IFA 2001 		Standard and Guidance for Archaeological Watching Briefs.