BAMBURGH RESEARCH PROJECT

MANOR COTTAGE,

EMBLETON,

NORTHUMBERLAND

REPORT OF ARCHAEOLOGICAL

MONITORING AND RECORDING

Compiled for Mrs Claire Reed by The Bamburgh Research Project: Commercial Projects Section

# BRP 08/09									October 2008

Contents:

SUMMARY										3

- Introduction								4

2.0	THE SITE									4

2.1	Location									4

##### 2.2	Archaeological background							4

3.0	METHODOLOGY								5

3.1	Monitoring during excavation						5

3.2	General standards								5

4.0	RESULTS									6

4.1	Monitoring during excavation						6

5.0	CONCLUSIONS								7

REFERENCES									8

APPENDIX I	WSI									9

Figure 1	Location of the development

Figure 2	Location of the new construction

# Plate 1		Excavated section of western foundation trench

# Plate 2		Excavation stopped at 1.7m

# SUMMARY

This report has been compiled by The Bamburgh Research Project for Mrs Claire Reed and sets out the results of the archaeological monitoring undertaken in August 2008, during the groundworks associated with the construction of an extension to Manor Cottage, Embleton, Northumberland (NGR NU 22952260) (Figures 1 and 2).

Excavation of the western foundation trench for the extension commenced on the 23rd of September and was suspended on the 24th of September 2008. The trench was excavated c. 0.7m wide and was dug down in a series of spits using a mini-digger. A series of layers of made ground of recent date were encountered, comprising topsoil to a depth of 0.4m over layers of rubble and stone fragments. Modern china, plastic and polythene indicated a 20th century date for the deposit sequence. Excavation continued to a depth of 1.7m when the reach of the machine arm became a limiting factor. A consultation between the contractor and the building inspector resulted in a decision being taken to alter the foundations to take into account the great depth of made-up material. The building foundations would be completed as a concrete raft at a depth of 0.5m below ground level and the excavated trench filled to this depth with building stone. The watching brief was therefore suspended following consultation with the Assistant County Archaeologist.

The house at Manor Cottage lay at the western extent of the village and on a part of the road that rose up towards the east with a noticeable gradient. The level platform for the house construction is likely to be the result of terracing into the natural gradient. The ground on the western, downhill, side being made up more than 1.7m. The excavation of the trench therefore revealed no features of archaeological interest, but equally must be seen as indicative of a very localised situation with regard to the preservation of archaeological features and the depth at which they may be encountered.

MANOR COTTAGE,

EMBLETON,

NORTHUMBERLAND

REPORT OF ARCHAEOLOGICAL MONITORING

- Introduction

    - This report has been compiled by The Bamburgh Research Project, Commercial Section for Mrs Claire Reed. The document sets out the results of the monitoring of the groundworks associated with the construction of an extension to Manor Cottage, Embleton, Northumberland, undertaken during the 23rd and 24th of September 2008.

1.0.2	The work was undertaken in compliance with a Written Schedule of Investigation compiled by the Bamburgh Research Project in September 2008 in response to a brief issued by the Northumberland County Council Conservation Team. The NCCCT reference number is: A16/2; 7851 and the Planning application number is: A2007/0545. The OASIS record number is: bamburgh1-49446.

2.0 	THE SITE

2.1	Location

2.1.1	Manor Cottage is located off Station Road within the western part of the village of Embleton, Northumberland, which lies on the B1339, some 9km to the south of Seahouses (NGR NU 22952260) (Figures 1 and 2).

  - Archaeological background

    - The village of Embleton is first mentioned in the records in the medieval period as the caput of the barony of Embleton, granted to the family of Odard of Bamburgh for three knights fees by Henry I.  The church of the Holy Trinity is of at least this date if not earlier, though has been much altered in later periods. A Moot Hall, Tower House and Hospital are also known to be present in the village from the medieval period. The Tower House lies some 170m to the south east of the proposed development and the hospital site may lie to the south of the village if the place name Spitalford is derived from this establishment.

## 2.2.2	Recent archaeological work, some 50m to the south of the development and to the south of Station Road demonstrated the presence of substantial archaeological remains of medieval occupation, including buildings along the street frontage and activity across the tofts to their rear.

    - The development area is within the village bounds at the time of the compilation of the first Edition Ordnance Survey c. 1860. As a result it is entirely possible that it lies within the extent of the medieval village.

3.0	METHODOLOGY

# 3.1	Monitoring during excavation

3.1.1	A suitably experienced archaeologist, familiar with the archaeological background to the site, was present to record any items of interest that were revealed. All work was carried out in compliance with the codes of practice of the Institute of Field Archaeologists (IFA) and followed the IFA Standards for Watching Briefs. The work undertaken conformed to the methodology listed below.

3.2	General standards

3.2.1	All archaeological features identified during the monitoring, would be sample excavated according to their type and form:

50% of all discrete features.

50% of waterlogged deposits.

25% of stratified deposits.

25% of the area of linear/curvilinear features with a non-uniform fill

10% of the area of linear/curvilinear features with a uniform fill

3.2.2	A 40 litre bulk palaeoenvironmental sample would be taken from all features recognised as suitable for the preservation of palaeoenvironmental remains.

3.2.3	Secure contexts would be sampled for dating where appropriate, whether on site or as sub samples of bulk samples.

3.2.4	Pottery and Animal Bone would be collected as bulk samples whilst significant artefacts would be three-dimensionally recorded prior to processing. All finds would be recorded and processed according to the BRP system and submitted for post-excavation assessment. Finds recovery and storage strategies were in accordance with published guidelines (English Heritage 1995 and IFA Guidelines for Finds Work). Had artefacts of gold or silver been recovered they would be treated in accordance with the 1996 Treasure Act and appropriate procedures would be followed.

3.2.5	In the event of Human burials being revealed they would be left in situ and treated in an appropriate manner. Consultation with the County Archaeological Officer would be sought to determine further action.

3.2.6	Any archaeological features encountered would be hand-cleaned, excavated and recorded:

- A photographic record of the site was taken using black and white print, colour slide film at 35mm format. In addition a digital photographic record was compiled.

- A written description of features was compiled using the BRP pro forma context recording system.

3.2.8	Arrangements will be made with the appropriate museum for the deposition of the site archive within 6 month of the completion of the post-excavation report.

4.0	RESULTS

  - Monitoring during excavation

4.1.1	Excavation of the western foundation trench for the extension commenced on the 23rd of September and was suspended on the 24th of September 2008. The trench was excavated c. 0.7m wide and was dug down in a series of spits using a mini-digger. A series of layers of made ground of recent date were encountered, comprising topsoil to a depth of 0.4m over layers of rubble and stone fragments. Modern china, plastic and polythene indicated a 20th century date for the deposit sequence. Excavation continued to a depth of 1.7m when the reach of the machine arm became a limiting factor. A consultation between the contractor and the building inspector resulted in a decision being taken to alter the foundations to take into account the great depth of made-up material. The building foundations would be completed as a concrete raft at a depth of 0.5m and the excavated trench filled to this depth with building stone. The watching brief was therefore suspended following consultation with the Assistant County Archaeologist.

.

5.0	CONCLUSIONS

    - The house at Manor Cottage lay at the western extent of the village and on a part of the road that rose up towards the east with a noticeable gradient. The level platform for the house construction is likely to be the result of terracing into the natural gradient. The ground on the western, downhill, side being made up more than 1.7m. The excavation of the trench therefore revealed no features of archaeological interest, but equally must be seen as indicative of a very localised situation with regard to the preservation of archaeological features and the depth at which they may be encountered.

Text and illustrations: Graeme Young

BRP 08/09									October 2008

REFERENCES

Published and unpublished sources

BRP			Finds Manual, 2000

BRP			Health and Safety Document

English Heritage	Management of Archaeological Projects 2, 1991.

English Heritage	A strategy for the Care and Investigation of Finds. Ancient Monuments Laboratory, 1995.

IFA 2000 		Code of Conduct

APPENDIX I

MANOR COTTAGE,

EMBLETON,

NORTHUMBERLAND

ARCHAEOLOGICAL WATCHING BRIEF

WRITTEN SCHEDULE OF INVESTIGATION

- Introduction

1.0.1	This Written Schedule of Investigation has been compiled by The Bamburgh Research Project for Mrs Claire Reed, regarding the construction of an extension to the building and new access arrangement at Manor Cottage, Embleton, Northumberland, during September 2008. The document sets out the project design for an archaeological watching brief to be conducted during groundworks associated with the construction.

    - The Written Schedule of Investigation details the proposed scheme of works for the watching brief and has been prepared in order to fulfil a requirement for the planning application, as laid out in the brief issued by The Northumberland County Council Conservation Team. The NCCCT reference number is: A16/2; 7851 and the Planning application number is: A2007/0545.

2.0 	THE SITE

2.1	Location

2.1.1	Manor Cottage is located off Station Road within the western part of the village of Embleton, Northumberland, which lies on the B1339, some 9km to the south of Seahouses (NGR NU 22952260) (Figures 1 and 2).

2.2	Archaeological background to the site

    - The village of Embleton is first mentioned in the records in the medieval period as the caput of the barony of Embleton, granted to the family of Odard of Bamburgh for three knights fees by Henry I.  The church of the Holy Trinity is of at least this date if not earlier, though has been much altered in later periods. A Moot Hall, Tower House and Hospital are also known to be present in the village from the medieval period. The Tower House lies some 170m to the south east of the proposed development and the hospital site may lie to the south of the village if the place name Spitalford is derived from this establishment.

## 2.2.2	Recent archaeological work, some 50m to the south of the development and to the south of Station Road demonstrated the presence of substantial archaeological remains of medieval occupation, including buildings along the street frontage and activity across the tofts to their rear.

    - The development area is within the village bounds at the time of the compilation of the first Edition Ordnance Survey c. 1860. As a result it is entirely possible that it lies within the extent of the medieval village.

  - Impact of the development

    - The development involves the construction of an extension within the north west corner of Manor Cottage and the creation of new access and parking arrangements. The extension to the building measures 5.4m by 4m and infills a gap in the L-shaped building. The new access arrangements involve the construction of retaining walls on the east and west sides of the new drive which will necessitate the levelling of the ground to an even 1 in 12 gradient and the construction of a new, wider, gate (Figure 2).

    - The foundations of the new extension to the building, insertion of the stone retaining walls and levelling work for the new driveway have the potential to impact on preserved archaeological stratigraphy on the site.

3.0	OBJECTIVES

    - In the light of the potential for the construction work to impact, in places, upon preserved archaeological remains it is proposed that a continuous watching brief be conducted during the ground work in accordance with the specification laid out in the brief issued by the County Council Conservation Team.

4.0	METHODOLOGY

4.1	Watching brief during excavation

    - During all excavation activity for the new development a suitably experienced archaeologist, familiar with the archaeological background to the site, will be present to record any items of interest that are revealed. Where appropriate all excavation and stripping will be carried out by a machine using a toothless ditching bucket. All work will be carried out in compliance with the codes of practice of the Institute of Field Archaeologists (IFA) and should follow the IFA Standards for Watching Briefs. This watching brief will conform to the following methodology.

4.2	Contingency

    - In the event of the discovery of unexpected archaeological remains over and above those predicted by previous archaeological work on the adjoining site, work will cease and the County Archaeological Officer/representative of the developer will be notified in order that an assessment of the importance of the remains and any provision for their recording may be made.

    - A contingency for excavation comprising up to 20 person days can be invoked following consultation with the County Archaeologist.

4.3	General standards

4.3.1	All archaeological features identified during the monitoring, or following the implementation of the contingency will be sample excavated according to their type and form:

50% of all discrete features.

50% of waterlogged deposits.

25% of stratified deposits.

25% of the area of linear/curvilinear features with a non-uniform fill

10% of the area of linear/curvilinear features with a uniform fill

4.3.2	A 40 litre bulk palaeoenvironmental sample will be taken from all features recognised as suitable for the preservation of palaeoenvironmental remains.

4.3.3	Secure contexts will be sampled for dating where appropriate, whether on site or as sub samples of bulk samples. Any concentrations of charcoal or other carbonised material recovered on site will usually be retained.

4.3.4	Pottery and Animal Bone will be collected as bulk samples whilst significant artefacts will be three-dimensionally recorded prior to processing. All finds will be recorded and processed according to the BRP system and submitted for post-excavation assessment. Finds recovery and storage strategies will be in accordance with published guidelines (English Heritage 1995 and IFA Guidelines for Finds Work). Should artefacts of gold or silver covered by the 1996 Treasure Act be recovered, appropriate procedures will be followed.

4.3.5	In the event of Human burials being revealed they will be left in situ and treated in an appropriate manner if possible. Any burial requiring excavation will be exposed, recorded and lifted in total. After consultation with the County Archaeological Officer, if excavation is required, work will comply with the relevant home Office regulations.

4.3.6	Any archaeological features encountered will be hand-cleaned, excavated and recorded:

- A photographic record of the site will be taken using black and white print, colour slide film at 35mm format. In addition a digital photographic record will be compiled.

- A written description of features will be recorded using the BRP pro forma context recording system.

- All features will be drawn at an appropriate scale using pre-printed permatrace. Plans will normally be drawn at a scale of 1:20 and sections at a scale of 1:10.

4.3.7	All archaeological features and horizons will be accurately tied into the Ordnance Survey grid. All levels will be tied in to Ordnance Datum.

4.3.8	Arrangements will be made with the appropriate museum for the deposition of the site archive within 6 month of the completion of the post-excavation report.

5.0	MONITORING

5.0.1	Access will be made available at all reasonable times to the archaeological representatives of the Northumberland County council Conservation Team to inspect the excavation site.

5.0.2	Access to the site will be on the basis of prior notification and subject to any relevant health and safety considerations.

6.0	POST-EXCAVATION WORK, ARCHIVE AND REPORT COMPILATION

6.0.1	On completion of the excavation an assessment of the site records and finds will be undertaken in accordance with English Heritage (1991) guidelines. This will include:

- collation of all site records

- compilation of a report

- production of context, photographic, finds and illustration databases

- analysis of the finds assemblage by relevant specialists

- environmental assessment of selected bulk samples

6.0.2	The assessment report, with each page and paragraph numbered and with cross referenced illustrations, will include:

- summary of the project background

- site location

- methodology

- results of the watching brief

- site location plans and illustrations of results at appropriate scales

- interpretation of the results in an appropriate context

- post-excavation assessment of the site archive

- catalogue and assessment of the artefactual archive

- catalogue and assessment of the faunal remains

- catalogue and assessment of the palaeoenvironmental samples recovered

- appendix containing a list and summary of each recorded context

6.0.3	A copy of the report should be submitted by the archaeologist to the commissioning client, and the County SMR within 2 months of completion of the work. A summary will be prepared for 'Archaeology in Northumberland' and an article will be submitted to a local or national journal if appropriate.

6.0.4	The site archive will be prepared to the standard specified in the Management of Archaeological Projects, appendix 3 (HBMC 1991) and in accordance with the Guidelines for the Preparation of Excavation Archives for Long Term Storage (UKIC 1990).  A summary account of the context record will be included and written by the supervising archaeologist. The archive will be deposited at the specified museum within 6 months of completion of the work on site.

6.0.4	An online OASIS form will be completed for the project as part of the post-excavation assessment process.

7.0	PERSONNEL

7.0.1	The designated project manager Graeme Young, is one of the five directors of the Bamburgh Research Project. A graduate of Newcastle University, with 18 years of experience in field archaeology including directing a number of excavations of urban medieval sites in Newcastle and Durham. He is an Associate Member of the Institute of Field Archaeologists.

7.0.2	Additional field staff, with appropriate archaeological experience, will be engaged as required.

8.0	SUB-CONTRACTED SPECIALISTS

    - Although it is not possible to predict the range of artefacts that may be recovered provision has been made for the analysis of the most common artefacts.

Material			Specialist

Medieval pottery			Jenny Vaughan

Post-medieval pottery		Jenny Vaughan

Prehistoric pottery		Blaise Vyner

Roman Pottery			Blaise Vyner

Animal bone			Durham University Archaeological Services

Palaeoenvironmental		Durham University Archaeological Services

Conservation			Karen Barker

9.0	HEALTH AND SAFETY

9.0.1	The Bamburgh Research Project complies with the 1974 Health and Safety Act and its subsequent amendments in all its operations. The SCAUM manual and the Bamburgh Research Project Health and Safety Policy Document is followed for all site works. A designated and appropriately trained first aider is present at all times during working hours. A First Aid kit, Accident Book and telephone are provided for each project. Safety footwear is mandatory on all excavation sites. Where required safety helmets and reflective jackets are provided. It is policy for a vehicle to be present at an excavation and staff must be appropriately equipped for bad weather.

9.0.2	All staff undergo a safety induction prior to commencing work on site. A written risk assessment is undertaken specific for each site. The safety assessment is reviewed on a daily basis and changes to the working conditions monitored continually during adverse weather conditions.

Text: Graeme Young.

BRP 08/09									September 2008

REFERENCES

Published and unpublished sources

Bateson E.		History of Northumberland I, 1893.

BRP			Finds Manual, 2000

BRP			Health and Safety Document

English Heritage		Management of Archaeological Projects 2, 1991.

English Heritage	A strategy for the Care and Investigation of Finds. Ancient Monuments Laboratory, 1995.

IFA 2000 		Code of Conduct

IFA 2001 		Standard and Guidance for Archaeological Watching Briefs.