SURVEY RESULTS

98 / 52 Smallhythe, Kent

1.	Survey Area

1.1	Three areas were selected for detailed area survey. Area A was surveyed using gradiometry, while Areas B and C were surveyed using both gradiometry and resistance. A fourth area was available for seismic refraction survey.

1.2	The survey grid was set out by GSB Prospection and tied in to existing field boundaries by GSB Prospection or RCHME.

2.	Display

2.1	The results are displayed as X-Y traces, dot density plots and grey scale images. These display formats are discussed in the Technical Information section, at the end of the text.

2.2	From the seismic data the depth to the interface beneath each geophone has been calculated providing a profile of the bedrock interface beneath the ground surface for the length of the survey line.

3.	General Considerations - Complicating factors

3.1	All three areas were generally free of obstacles, although the vegetation from  part of Area A had to be cut down prior to survey.

4.	Results of Survey

4.1.	Area A

It was believed that industrial activity associated with ship building may be present within this field.

Gradiometer Survey

4.1.1	Initially the whole of this field was scanned at 10m intervals. The scanning suggested that few magnetic anomalies were present. However, a concentration of very strong anomalies was found toward the north eastern corner of the field. Detailed survey was carried out here.

4.1.2	The detailed gradiometer survey data indicates a large area of ferrous type responses. The main zone of this response coincides with a large patch of nettles, which was cut down prior to survey. The farmer indicated that a ‘scoop’ in the field at this point had been partially filled in a decade or so ago.  An additional area of ferrous type response was also noted to the west of this zone, while to the east an area of increased noise was found.

4.1.3	The interpretation of these anomalies was consistent with the archaeological expectation for the field. That is, the anomalies could indicate industrial activity. However, modern ferrous material was noted in the grass and a trench excavated through the western ferrous anomaly proved to be filled with modern material.

4.2	Area B

Limited magnetic and resistance survey was initially undertaken over a 40 x 40m block where Stewart Ainswortb, of RCHME,  had identified low earthworks that may indicate docks or slipways. This field is next to the present village of Smallhythe.

Resistance Survey

4.2.1	There is a clear divide in the resistance survey data with an area of high resistance approximately parallel with the modern field. This was interpreted as an edge to the river, possibly either indicating dry river silts or sand. It was not possible to be precise about the exact position of the edge as the high resistance anomaly changed gradually into the lower background.

4.2.2	There are a number of anomalies within the northern part of the survey. However, most of them do not appear to correlate very well with the earthworks. A single high resistance anomaly was noted on the edge of one of the earthworks and this also produced a significant magnetic response (see below). By itself this isolated response could not be interpreted archaeologically.

Gradiometer Survey

4.2.3	The original survey covered the same 40 x 40 m block as reported on for the resistance survey. The most significant response within this 40m block is a very strong, broad magnetic anomaly that coincides with the isolated high resistance response. It was believed that fired or heavily burnt material would be present at this point.

4.2.4	Near to the ‘burnt’ feature are a few other anomalies that appear to correlate with the ‘slipways’. There is also a vague but real decrease in the background response at the southern edge and this covers the same area as the supposed river edge found in the resistance data.

At this point an excavation was opened over the presumed burnt / fired response. Once it was established that the response did indicate significant fired material the gradiometer survey was then expanded to place the findings in a wider context.

4.2.5	The extended survey, largely to the north and east of the original 40 x 40 m block, has provided conclusive evidence for archaeological activity. The anomalies are very strong and are likely to relate to both industrial processes and settlement.

4.2.6	Despite the wealth of evidence for archaeological type responses, a detailed interpretation is still difficult. This is a result of the nature of the archaeology and the combination of magnetic responses from interacting anomalies. In some instances it has only been possible to identify ‘zones of increased response’ rather than individual anomalies. In such an area the archaeology is likely to be relatively complex, possibly suggesting dense or multi-phase settlement.

4.2.7	While no further fired responses have definitely been identified, some of the individual anomalies, especially at the northern end of the survey, may have some archaeological potential.

4.2.8	Some ditch type anomalies have been located and it is assumed that they indicate land divisions associated with the settlement and presumed industrial activity.

4.2.9	A trench positioned over the change in resistance at the southern edge of the field revealed the presence of a former shoreline. An excavation over the fired response was also very fruitful, with a substantial brick kiln found at this point.

4.3.	Area C

This area was considered for survey as a result of the possible dock in the National Trust land directly to the west. An initial scan suggested a number of possible anomalies in the western part of the field. Both gradiometry and resistance survey were  carried out here.

Gradiometer Survey

4.3.1.	Detailed survey revealed that the majority of the anomalies lie in the western part of the survey. A large ferrous type anomaly was believed to be of some interest, especially as it appeared to be associated with a magnetic positive to the east and a high resistance anomaly (see below). In the near vicinity of these anomalies are a number of pit and ditch type responses.

Resistance Survey

4.3.2.	As with the magnetic data the major anomalies are within the western part of the survey. The high resistance itself is part of elevated values which spreads across 10 - 15m. The impression given is that potentially burnt deposits lie on an area of drier, perhaps higher, land.

4.3.3.	Other high resistance anomalies trend in the same orientation as those noted on the gradiometer. These may represent ploughed out land divisions.

4.3.4.	Excavation over the massive ferrous response and the associated high magnetic anomaly provided many finds. The ferrous response was partially the result of a concentration of ship nails, but mostly the product of a large, and reasonably recently buried, kettle. The high magnetic anomaly appeared to be a ‘scoop’ or pit which contained many iron nails.

5.	Seismic Refraction Survey

5.1.	A seismic refraction survey was carried out along a 180m transect, made up of three spreads with geophones at 5m intervals. Survey was undertaken as a conventional four shot refraction survey. Although a 24 channel seismograph was used, only 12 channels were available for data collection at the time. A hammer and plate was used as the source, although trials were undertaken using a buffalo gun. There was, however, no significant difference between the gun source and the hammer source and as a result the hammer was used in the interest of speed.

5.2.	The data indicate the presence of two possible palaeochannels. One is approximately 45m wide and 10m deep and the other approximately 120m wide with a dipping base which reaches a maximum depth of 30m shallowing to 20m in the south. The nature of the profile and its correlation with known borehole data suggests that the bedrock interface has been defined.

5.3.	No information regarding the nature of stratification within the channels is available from the data. This is primarily due to the limitations of the technique. Seismic refraction relies on two basic assumptions: velocity increases with depth and boundaries between different materials form a distinct interface. Borehole data along the seismic traverse confirmed that the deposits comprise alternating layers of material which is likely to result in some layers having a slower velocity than the one above. In such situations this layer becomes ‘hidden’. Aside from reducing the resolution of the technique it also introduces errors into the depth calculation because layers with differing velocities are grouped together resulting in an overestimation of the depth to the interface. Given the nature of a floodplain one would expect there to be gradual lateral and vertical variations within the sediments. Again, if these do not form distinct boundaries this finer detail is lost. While this finer detail could normally be obtained using a GPR survey the saturated nature of the deposits made that technique unfeasible.

6.	Conclusions

6.1.	The gradiometer in particular has established the position of many areas of archaeological interest. Trenching revealed features of considerable archaeological interest in two of the areas (B and C). The features were largely industrial in nature, although the gradiometer response in Area 2 suggests that an extensive area of settlement has also been found. The resistance results were supportive of the magnetic data and helped establish the position of a former shoreline.

6.2.	The seismic refraction survey has identified two possible channels one 45m wide and 10m deep and the other 120m wide and 30m at its greatest depth. However these depths are approximate, the interface may not be as deep. The depth of the detected interface and comparison with known boreholes in the area suggests that it is the bedrock interface which has been detected.

Project Team	:	Dr C F Gaffney, J Gater, Dr S Ovenden-Wilson, J Nicholls & A Shields

Date of Survey:		2nd-4th June 1998

Date of Report:		7th August 1998

References:

SSEW 1983.	Soils of England and Wales. Sheet 6, South East England. Soil Survey of England 		and Wales.

SITE SUMMARY SHEET

98 / 52 Smallhythe, Kent

NGR: TQ 892 300

Location, topography and geology

The four survey areas covered by this report lie at the southern limit of the village of Smallhythe, Kent. The B2082 road runs north south through the village and three of the surveys are on the western side of the road while the other is adjacent to the National Trust museum on the eastern side. All of the fields were slightly sloping down to the south, with the line of a seismic survey cutting across part of the former flood plain of the River Rother. The soils are of the Whickham 1 association and are slowly permeable seasonally waterlogged fine silty over clayey, fine loamy over clayey soils (SSEW 1983). Such soils should produce only a moderate magnetic response.

Archaeology

Smallhythe, while only a small village at present, is documented as a vibrant centre during the medieval period. Its prominence is, despite being situated a great distance from the coast, largely the result of a thriving port and associated shipbuilding.

Aims of Survey

It was hoped that the surveys could establish areas of potential industrial activity associated with the shipbuilding, obtain information on the depth and width of palaeochannels next to the town and find some evidence for potential settlement. The surveys were conducted as part of a Time Team investigation by Channel 4. The programme is scheduled to be broadcast during 1999.

Summary of Results *

The geophysical data provided considerable help in locating areas of archaeological potential. The interpretation of the data suggested that industrial and settlement features are likely to be present within the survey areas. While one of the trenches found only modern ferrous material, the other trenches based on the geophysical data were very productive. A kiln, ditches / pits, significant numbers of iron artefacts and a previous shoreline were all revealed as a result of the gradiometer and resistance surveys. Gradiometer survey also indicated a large area of likely settlement next to the present village.

The seismic refraction survey has successfully identified two channels which correspond well with borehole data in the area. The results show what appears to be the interface between the sediments and the bedrock. Finer detail such re-cut channels was beyond the resolution of the technique.

* It is essential that this summary is read in conjunction with the detailed results of the survey.

List of Figures

Figure 1		Survey locations							1:3000

Figure 2		Summary interpretation, Areas A - C				1:3000

Figure A.1	Area A: Data and interpretation					1:500

Figure B.1	Area B: Gradiometer and resistance comparison			1:500

Figure B.2	Area B: Resistance interpretation					1:500

Figure B.3	Area B: Gradiometer data, dot density and X-Y plot			1:1000

Figure B.4 	Area B: Gradiometer data, greyscale				1:1000

Figure B.5	Area B: Gradiometer interpretation					1:1000

Figure C.1	Area C: Gradiometer data, greyscale				1:500

Figure C.2	Area C: Gradiometer  data, dot density				1:500

Figure C.3	Area C: Gradiometer data, X-Y plot				1:500

Figure C.4	Area C: Gradiometer interpretation					1:500

Figure C.5	Area C: Resistance data, greyscale					1:500

Figure C.6	Area C: Gradiometer and resistance comparison			NTS

Figure C.7	Area C: Resistance interpretation					1:500

Figure D.1	Seismic refraction profile						NTS